## Slide 1
Automatic Speaker Equalization System
Results
Sound-Sifter
1 MEASUREMENT PHASE
Fourier Transform
Log Swept Sine
Hz
dB
First, a swept sine or “chirp” is played through the speakers. This signal goes from 20Hz to 20kHz.
The microphone captures the sweep, resulting in an impulse response.
Then the frequency response is obtained by taking the Fourier Transform of the impulse.
Measured Frequency Response
Samuel Bhushan
bhushan.samuel@gmail.com
Hailey Parkin
hrparkin@gmail.com
Introduction
Think about all of the places you hear audio throughout the day. From noisy coffee shops to carefully controlled movie theaters, our experience with speakers varies drastically. Sometimes the music creates a welcoming soundscape, but often you are just wishing someone would turn the volume down. It is likely that the quality of the sound, and not just what’s being played, that reduces your enjoyment. Many of these quality issues cannot be solved by simply purchasing better speakers, and need the room to be physically modified. Using signal processing, our project aims to improve your listening experience without the need to change your room or speakers.
2 CORRECTION PHASE
The frequency response from the measurement phase is divided into smaller frequency bands.
Then the bands are analyzed and the largest deviating bands are identified.
A reverse filter is created that addresses these problem bands. This is done by applying an inverting peak that cancels out the response.
Hz
dB
Hz
dB
Identify Problems
Create Inverse Filter
Overall System Diagram
BeagleBone
+
Audio Cape
Audio In
Loudspeakers
Microphone
3 FILTERATION PHASE
Calculated Filter
Audio Input
Hz
dB
Corrected Frequency Response
Audio destined for the speaker first goes through the inverse filter, correcting the output.
Filtering Subsystem
CPU
Sound Card
Speaker
Audio In
ADC
Signal Processing
DAC
Speaker
DAC
Sound Card
Sine Sweep
MIC
DAC
CPU
Fourier Transform
Calibration Subsystem
The calibration subsystem computes a high resolution response of the room. A million point FFT creates an accurate frequency response based on the measurement.
The processor has the capacity to implement filters for correction on up to __ frequency bands.
A audible difference can be heard before and after filtering when the adjustments needed are significant.
Future Expansion
The system package could be modified to include smaller units that implement just the filtering. This would allow to Sound-Sifter to be used for multiple rooms without the cost of a microphone and calibration processing for each room.
Additionally, the Sound-Sifter does not currently identify if room defects are specifically due to reverberation. Additional algorithms could be included to better correct these problems.
Parts
BeagleBone
a credit-card sized Linux computer